## Slide 1
BIRDS-4 FM
APRS Long Range Test Report
Prepared by:
Marloun P. Sejera
15 December 2019

## Slide 2: CONTENTS
Antenna Orientation
Effective Downlink Attenuation (EDA)
Effective Uplink Attenuation (EUA)
Uplink Sensitivity Test
Link Budget

## Slide 3: Antenna Orientation
Satellite was placed on the platform facing KyuTech GS with azimuth of 400. VHF dipole is oriented horizontally
HORYU antenna was rotated facing Mt. Sarakaura.
BIRDS-4 FM (JP) at Mt. Sarakura, facing KyuTech GS. VHF dipole (tuned at 146 MHz) is oriented horizontally
VHF dipole

## Slide 4: Effective Downlink Attenuation (EDA)
At Mt. Sarakura side, Kenwood TH-D72 hand-held radio (HHR) transmitted carrier signal (145.825 MHz) using dipole reference.
At KyuTech GS side, received power was measured using spectrum analyzer (SA).
Kenwood TH-D72
Reference dipole*
HORYU antenna
Spectrum Analyzer
KyuTech GS side
Mt. Satakura side
Kenwood TH-D72
Reference dipole*
*Photo shows UHF reference dipole. Actual photo of VHF reference dipole is not available
EDA = PTX (HHR) – PRX (SA)
EDA = 36 dBm – (-40 dBm)
EDA = 76 dB

## Slide 5: Effective Uplink Attenuation (EUA)
At KyuTech GS side, Kenwood TH-D72 hand-held radio (HHR) was used to transmit carrier signal (145.825 MHz).
At Mt. Sarakura side, received power was measured using spectrum analyzer (SA).
HORYU antenna
Kenwood TH-D72
KyuTech GS side
Mt. Satakura side
Spectrum Analyzer
Reference dipole*
*Photo shows UHF reference dipole. Actual photo of VHF reference dipole is not available
EUA = PTX (HHR) – PRX (SA)
EUA = 25.5 dBm – (-50 dBm)
EUA = 75.5 dB

## Slide 6: Effective Attenuation Summary
Effective Attenuation | FM (JP) | EM
Uplink (EUA) | 75.5 dB | 70.8 dB
Downlink (EDA) | 76 dB | 71.8 dB
BIRDS-4 FM effective attenuation (EUA and EDA) are almost similar.
Note:
For uplink, reference dipole was used to measure received signal and not satellite’s VHF dipole.
For downlink, HHR transmitted the signal and not from the satellite.

## Slide 7: Uplink Sensitivity Test Setup
GS sends message using HHR. When ACK from satellite is received, it is considered success. Uplink command is sent 10 times .
Additional attenuator is placed and test is again conducted. This is repeated until success rate is zero.
Uplink sensitivity is defined at 50% success rate.
BIRDS4 FM
Att.
Kenwood
TH-D72
HORYU
antenna
25.5 dBm

## Slide 8: Uplink Sensitivity Test Result
Added Attenuators in GS | Total Attenuation | PRX at Mt. Sarakura (estimated) | Success Rate
40 dB | 115.5 dB | -90 dBm | 10/10
42 dB | 117.5 dB | -92 dBm | 10/10
45 dB | 120.5 dB | -95 dBm | 9/10
46 dB | 121.5 dB | -96dBm | 6/10
47 dB | 122.5 dB | -97 dBm | 0/10
PTX (GS): 25.5 dBm
EUA: 75.5 dB
Total Attenuation = EUA + Added Attenuators
PRX (estimated) = PT (GS) – Total Attenuation

## Slide 9: Uplink Sensitivity Comparison
Uplink Sensitivity | FM (JP) | EM
 | -96 dBm | -95 dBm
There is no significant difference on the uplink sensitivity of FM and EM satellites.
There is no significant improvement in uplink sensitivity when aluminium sheet is placed at the back of VHF TRX as an RF shield.

## Slide 10: UpLink Budget
With the same setup as long range test at Mt. Sarakura except Pt = 37 dBm, successful uplink can be achieved at elevation angle of at least 300

## Slide 11: UpLink Budget (Ground Station Setup)
With 50W radio output power and 16 dB antenna gain, uplink success can be achieved at 100 elevation.

## Slide 12: UpLink Budget (HHR setup)
With 5W radio output power and 7 dBi antenna gain, uplink success cannot be achieved even at high elevation angle.

## Slide 13: DownLink Budget
-105 dBm was based on BIRDS-2 test with satellite in orbit.
Successful downlink can be achieved even at 150 elevation.